## Slide 1: Instruction format of x86
Presented by:
- Hifza Hussain awan
- Waleed bin riaz
- Skander khan

## Slide 2
8086 instruction format
1 byte to 6 byte in length
Length of byte in dependent on addressing mode
Instruction byte contain
  OP code
  Addressing mode
    2 byte for effective addressing
    1 or 2 byte displacetment
    1 or 2 byte immediate operand

## Slide 3
The upper block shows us the all six bytes
Every byte has 8 bits
Every byte has different functionality and is related to each other
Byte 1 | Byte 2 | Byte 3 | Byte 4 | Byte 5 | Byte 6

## Slide 4: Byte 1
It has eight bits
First six bits are specified for op code which contain the basic instruction of the operation
  OP stands for operation code
The seventh bit stores the direction of instruction
It has two condition
  If D= 1 instruction source is in register
  if D= 0 instruction destination is in register
The eighth bit stores the type of instruction: it has also two condition
  If W= 1 instruction operates on word data
  If W= 0 instruction operates on bytes data
opcode | w | w

## Slide 5
Byte 2
OP code
It contains three bits which are S , V , Z
S is sign extension
  If S=0 , no sign extension. It will continue with eight bits i.e no overflow
  If S=1 sign extended eight bits immediate sixteen. If W=1 from the first byte
V is shift and rotate
  If V=0 shift , rotate counts 1
  If V=1 shift or rotate specified in CL
Z is for conditional or loop statement. It will compare bit with zero flag
  If Z=0 repeat or loop for clear zero flag
  If Z=1 set zero flag

## Slide 6
Mode
It contains two bits which are also called two operands
One operand is the memory or both operands are In registers
00 | Memory mode
01 | Memory mode
10 | Memory mode
11 | Register mode

## Slide 7
R / M
It depends upon the mode bits
It also called effective addressing
Operands | Mode=00 | Mode=01 | Mode=10
000 | Bx + si | Bx + si+ 8 bits | Bx + si + 16 bits
001 | Bx + di | Bx + di + 8 bits | Bx + di + 16 bits
010 | Bp+ si | Bp+ si + 8 bits | Bp+ si + 16 bits
011 | Bp + di | Bp + di + 8 bits | Bp + di + 16 bits
100 | Si | Si + 8 bits | Si + 16 bits
101 | di | Di + 8 bits | Di + 16 bits
110 | Dir of address | Bp+ 8 bits | Bp + 16 bits
111 | Bx | Bx +8 bits | Bx + 16 bits

## Slide 8
Operands | If w=0 | If w=1
000 | Al | Ax
001 | Cl | Cx
010 | Dl | Dx
011 | Bl | Bx
100 | Ah | Sp
101 | Ch | bp
110 | Dh | Si
111 | Bh | Di
When mode values are 11 then we will do addressing using the following table:

## Slide 9
Byte 3:
When the operation is being performed on the bytes means the w form the first byte equals to 0 then we will use the bytes upto 3 as it has 8 bit displacement
Byte 4:
When the operation is being performed on the whole word means the w form the first byte equals to 1 then we will use the bits upto 4 as it has 16 bit displacement
low-order Displacement
High-order Displacement

## Slide 10
Byte 5:
low-order Operand
In that byte we will store the low order operands
  For example: if we have a value
  ( Mov ax,1234H)
  That 34 will be save in that low order operand.
Byte 6:
In that byte we will store the high order operands
  For example: if we carry the same upper example( Mov ax,1234H) then now in that bit 12 will be saved
High-order Operand

## Slide 11
Register Organization
CPU must have some working space (temporary memory) called Registers.
A computer systems employs a hierarchy of memory.
At the highest level of hierarchy memory is faster, efficient and smaller.
Within the cpu there is a set of registers which can be treated as a memory highest level of hierarchy.

## Slide 12
Register Organization
The registers in the CPU can be categorized into two groups which are following
User-visible Registers:
-These enables the machine or assembly language programmer to minimize main memory by optimizing use of registers.
Control and status registers:
-These are used by the control unit to control the operations of the CPU
-Operating systems programs also use them to control the execution of processes.

## Slide 13
USER VISIBLE REGISTERS
General Purpose
Data
Address

## Slide 14
1. General Purpose Registers:
Used for variety of functions by programmers.
Sometimes used for holding data of an instruction.
2. Data Registers:
Use only to hold and manipulate the data.
Cannot be employed in calculation of an operand address.
3. Address Registers:
Address registers only carry the address of data
Segment pointers are use to carry the address of base of data further the segment pointer is used to carry the address of diff segments i.e address of code segment or address of data segment.
As SI is used to carry the address of first index of array.

## Slide 15
Control and Status Registers
-Four registers are essential for this:
1. Program Counter(PC):
- Contains the address of instruction to be fetched.
Instruction Register(IR):
- Contains the instruction most recently fetched.
Memory Address Register(MAR):
- Contains the address of location of main memory from where the information has to be fetched or has to be stored.
Memory Buffer Register(MBR):
- Contains a word of data to be written or the word most recently used.

## Slide 16
Features of ARM instructions
All instructions are 32 bits long
Most instructions execute in single cycle
Every instruction can be conditionally executed
A load\store architecture
  Data processing instructions acts only on registers
  Three operand format
  Combined ALU and shifter for high speed bit manipulation

## Slide 17
Types of instructions
Data processing instructions
Data transfer instructions
Control flow instructions

## Slide 18
Data processing instructions
Arithmetic operations:
ADD r0,r1,r2 ;r0=r1+r2
SUB r0,r1,r2 ;r0=r1-r2
SBC r0,r1,r2 ;r0=r1-r2+C-1
RSB r0,r1,r2 ;r0=r2-r1
Logical operations:
AND r0,r1,r2 ;r0=r1ANDr2
ORR r0,r1,r2 ;r0=r1ORr2
XOR r0,r1,r2 ;r0=r1XORr2

## Slide 19
Register movement operations:
MOV r0,r1 ;r0=r2
MVN r0,r1 ;r0= NOT r2 :: move 1’s complement
Compare operations:
it includes the compare instructions which we use to compare to values:
CMP r1,r2
Shift registers operands:
ADD r3,r2,LSL#3 :it shows that add r2 in r2 and shift it to 3 bits from left ad store it in r3.

## Slide 20
Data transfer instructions
Three basic forms to move data between ARM reg and memory:
Single register load and store instruction
Multiple register load and store instruction
  To save or restore workspace registers for procedure entry exit
Single registers swap instructions
  It is used when you have to use the data present in memory then we will swap the data from memory to register to perform operations on it
Control flow instructions:
It includes the conditional statements:
loop statements
Compare statements

## Slide 21
Requirements placed on the processor
Fetch instruction: The processor reads an instruction from memory (register, cache, main memory)
Interpret instruction: The instruction is decoded to determine which action is required
Fetch data: The execution of an instruction may require reading data from memory
Process data: The execution of any process requires some logical or arithmetic operations on data
Write data: The result of any process requires riting data to memory

## Slide 22
COMPONENTS OF PROCESSOR
The major components of the processor are an arithmetic and logical uni (ALU) and a control unit (CU)
The ALU does the actual computation or processing of data
The control unit controls the movement of instruction in and out of the processor and controls the operations of ALU
Registers consists of the set of storage locations