## Slide 1: Addressing mode
Addressing mode and its type in assembly language

## Slide 2
Addressing mode
Specifies the location of data for instructions in assembly language.
Different ways by which CPU can access data or operands.
Where is the data?
How data is fetched?

## Slide 3
Addressing Modes Enable:
Data Manipulation
  Perform arithmetic and logical operations on data values.
Memory Access
  Read from and write to memory locations efficiently.
Operand Flexibility
  Choose suitable addressing modes based on instruction requirements and data manipulation needs.
Efficient Code Execution
  Optimize memory access patterns, reduce instructions, and minimize overhead.
Program Flow Control:
  Control program flow with branches and jumps based on relative offsets or conditions.

## Slide 4
Instruction’s type
ZERO-OPERAND INSTRUCTIONS:
HLT (halt the program execution)
CLC (clear carry flag).
TWO-OPERAND INSTRUCTIONS
This instruction adds the value of the source operand to the destination operand and stores the result in the destination operand.
Example usage: ADD BX, AX (adds the value in the AX register to the value in the BX register and stores the result in BX)
ONE-OPERAND INSTRUCTIONS
INC AX .
DEC AX ,
NEG DX

## Slide 5
TYPES OF ADDRESSING MODE
  Register addressing: operand is in a register
  Immediate addressing: operand is stored in the instruction itself
  Memory addressing: operand is in memory
    Direct addressing: Address field contains address of operand
    Indirect Addressing: The address field points to a memory cell containing the operand's address.

## Slide 6
Register Addressing
Register contains the operand.
Example:
MOV DX, BX
ADD DX,AX
The address field of the instruction refers to a CPU register that contains the operand.
No reference to memory is required to fetch the operand.
Opcode
Operand
Registers
Register
Instruction

## Slide 7
Immediate addressing
In immediate addressing, the second operand of the instruction is a constant.
Operand, data or value is directly specified within the instruction itself.
Example: mov ax, 5
  Add the constant value 5 to register ax
  5 is a constant value
Constant Value

## Slide 8
Advantages
Limitations:
No need to access memory or registers.
Avoids the need for memory access or registers, improving efficiency.
Useful for simple calculations, or immediate data manipulation.
Fast and Limited range
Values cannot change throughout the program

## Slide 9
Direct addressing
Use variable name for direct addressing
Example: mov ax , var1
Variables defined in data section
Assembler computes offset of variable
Example: MOV var2
Access data from specific memory location.
Example: MOV ,[2000]
Operand
Memory
Opcode
Memory Address
Instruction

## Slide 10
Advantages
Efficient for accessing memory locations with known addresses.
Limitations:
Limited flexibility as it can only access specific memory locations directly.
Requires fewer instructions compared to indirect addressing mode.
Inconvenient for accessing complex data structures or arrays.

## Slide 11
InDirect addressing
The address field points to a memory cell containing the operand's address.
Multiple memory accesses to find operand
It is commonly used for accessing data structures, arrays, or variables stored at different memory addresses.
Example: MOV AX, [BX]
BX holds the memory address.
Copy contents of memory location pointed to by register BX to register AX.
Opcode
Operand
Memory
Register
Instruction

## Slide 12
Advantages
Provides flexibility by allowing the use of memory locations stored in registers or memory locations.
Limitations:
Requires additional instructions for loading the indirect address.
Slightly slower compared to direct addressing due to the additional memory access required for indirection.
Suitable for accessing data structures, arrays, or dynamically determined memory locations.

## Slide 13
THANK YOU