## Slide 2
PRESENTED BY
ANUM IFTIHAR
(21-ARID-920)
SAIF ABBAS
(21-ARID-518)

## Slide 3: OPERANDS IN 8086

## Slide 4: TYPES

## Slide 5
REGISTER OPERAND
Register operands involve using the general-purpose registers of the 8086 processor, such as AX, BX, CX, DX, SI, DI, BP, and SP.
Example
MOV AX, BX
  Move the value of BX register into AX register
ADD CX, DX
  Add the value of DX register to CX register

## Slide 6
IMMEDIATE OPERAND
Immediate operands are constant values specified directly in the instruction itself.
Example
MOV AX, 1234h
  Move the immediate value 1234h into AX register
SUB CX, 10
  Subtract the immediate value 10 from CX register

## Slide 7
INDEXED OPERAND
Indexed operands allow to access memory using an index register in combination with an offset. The index register (SI or DI) is added to or subtracted from the offset to calculate the effective address.
Example
MOV AX, [SI + 10]
  Move the value stored at the memory location pointed by SI+10 into AX register

## Slide 8
BASE PLUS INDEX OPERAND
Base plus index operand uses an addressing mode that involves adding a base register (BX or BP) and an index register (SI or DI) to an offset to calculate the effective address.
Example
MOV AX, [BX + SI]
  Move the value stored at the memory location pointed by BX+SI into AX register

## Slide 9
PORT OPERAND
The 8086 can also perform input and output operations to communicate with external devices. Port operands are used to specify the input/output ports for these operations. Port addresses are treated as immediate operands.
Example
IN AL, 60h
  Input a byte from port 60h and store it in AL register

## Slide 10: MIPS

## Slide 11
DEFINITION
MIPS (Microprocessor without Interlocked Pipeline Stages). MIPS architecture was developed by MIPS Technologies (formerly MIPS Computer Systems) in the 1980s. the term "without interlocked pipeline stages" refers to a design characteristic where the pipeline stages of the microprocessor are not interlocked or dependent on each other for the execution of instructions. the MIPS architecture enabling higher instruction throughput and improved performance in executing instructions.

## Slide 12: DATA TYPES

## Slide 13
Byte (8 bits): Signed or unsigned integer values within the range of -128 to 127 (signed) or 0 to 255 (unsigned).
Halfword (16 bits): Signed or unsigned integer values within the range of -32,768 to 32,767 (signed) or 0 to 65,535 (unsigned).
Word (32 bits): Signed or unsigned integer values within the range of -2,147,483,648 to 2,147,483,647 (signed) or 0 to 4,294,967,295 (unsigned).
Floating-Point: 32-bit floating-point values following the IEEE 754 standard for representing real numbers.
Double Precision: 64-bit floating-point values following the IEEE 754 standard.

## Slide 14
Floating-Point
Smallest Positive Value: 1.17549435 x 10^(-38)
Largest Positive Value: 3.40282347 x 10^38
Smallest Negative Value: -1.17549435 x 10^(-38)
Largest Negative Value: -3.40282347 x 10^38
Example
Binary Representation: 0 10000010 01000000000000000000000
Sign Bit (S): 0 (positive number)
Exponent (E): 10000010 (130 in decimal)
Mantissa (M): 01000000000000000000000
The exponent is obtained by subtracting the bias value (127) from the binary value of the exponent field. So, the actual exponent is 130 - 127 = 3
To calculate the decimal value of this floating-point number, we use the formula:
(-1)^S * (1.M) * 2^(E - Bias)
Plugging in the values: (-1)^0 * (1.01000000000000000000000) * 2^(3 - 127)
The resulting decimal value is approximately 10.5

## Slide 15
Double-Precision
Smallest Positive Value: 2.2250738585072014 x 10^(-308)
Largest Positive Value: 1.7976931348623157 x 10^308
Smallest Negative Value: -2.2250738585072014 x 10^(-308)
Largest Negative Value: -1.7976931348623157 x 10^308
Example
Binary Representation: 0 10000000001 1000000000000000000000000000000000000000000000000000
Sign Bit (S): 0 (positive number)
Exponent (E): 10000000001 (1025 in decimal)
Mantissa (M): 1000000000000000000000000000000000000000000000000000
The actual exponent is obtained by subtracting the bias value (1023) from the binary value of the exponent field. So, the actual exponent is 1025 - 1023 = 2
Using the formula for decimal conversion: (-1)^S * (1.M) * 2^(E - Bias)
Plugging in the values: (-1)^0 * (1.1000000000000000000000000000000000000000000000000000) * 2^(2 - 1023)
The resulting decimal value is approximately 3.75

## Slide 16: OPERATIONS

## Slide 17
Load: Loads a value from memory into a register. For example, lw (load word), lb (load byte), lbu (load byte unsigned).
Store: Stores a value from a register into memory. For example, sw (store word), sb (store byte).
Arithmetic: Arithmetic operations on registers, such as addition (add), subtraction (sub), multiplication (mul), and division (div).
Logic: Logical operations, including bitwise AND (and), OR (or), XOR (xor), and shift operations (sll, srl).
Data Transfer: Operations for moving data between registers, such as moving values between registers (move) or swapping register values (swap).
Floating-Point: Operations for floating-point arithmetic, including addition (add.s), subtraction (sub.s), multiplication (mul.s), and division (div.s) for single-precision floating-point numbers.
Double-Precision: Operations for double-precision arithmetic, including addition (add.d), subtraction (sub.d), multiplication (mul.d), and division (div.d) for double-precision floating-point numbers.

## Slide 18: THANK
YOU !