## Slide 1: Shift Instructions
MUHAMMAD SAFI ULLAH (21-ARID-471)
Asneef (21-ARID-)
Presented by

## Slide 2: Shift Instructions
The shift instruction is used to shift the bits of a binary number to the left or right.
shift instruction is used when we load the data into the registers.

## Slide 3: Logical Shift Left
0 | 0 | 0 | 0 | 1 | 0 | 1 | 0
0 | 0 | 0 | 1 | 0 | 1 | 0 | 0
In a left shift, the bits of a binary number are shifted towards the left.
A left shift generally denotes multiplication of 2

## Slide 4: Logical Shift right
0 | 0 | 0 | 0 | 1 | 0 | 1 | 0
0 | 0 | 0 | 0 | 0 | 1 | 0 | 1
In a right shift, the bits of a binary number are shifted towards the right
A right shift generally denotes division of 2

## Slide 5: Arithmetic Shift right
1 | 0 | 1 | 0 | 0 | 0 | 1 | 1
1 | 1 | 0 | 1 | 0 | 0 | 0 | 1
In a right shift, the bits of a binary number are shifted towards the right
A left first bit denotes the sign and we copy the first bit into the second bit
sign

## Slide 6: Arithmetic Shift Left
0 | 0 | 0 | 0 | 1 | 0 | 1 | 0
0 | 0 | 0 | 1 | 0 | 1 | 0 | 0
Arithmetic shift left is same as logical shift left

## Slide 7: Rotate Right
0 | 0 | 0 | 0 | 1 | 0 | 1 | 0
0 | 0 | 0 | 0 | 0 | 1 | 0 | 1
In a Rotate right, the bits of a binary number are shifted towards the right
But the last bit is not wasted and it move to the start.

## Slide 8: Rotate Left
1 | 0 | 1 | 0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 1 | 1 | 0 | 1
In a left shift, the bits of a binary number are shifted towards the left.
But the first bit is not wasted and it move to the end.

## Slide 9: Rotate Right Through Carry
0 | 0 | 0 | 0 | 1 | 0 | 1 | 0
0 | 0 | 0 | 0 | 0 | 1 | 0 | 1
In a right shift, the bits of a binary number are shifted towards the right
Last bit move to carry.
1
0

## Slide 10: Rotate Left Through Carry
1 | 0 | 1 | 0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 1 | 1 | 0 | 1
In a left shift, the bits of a binary number are shifted towards the left.
But the carry move to the end.
1
1

## Slide 11
  THANK YOU