## Slide 1: Group Members
Zarar Shahid 21-ARID-532
Ahtisham Maqsood 21-ARID-408
Shamaila Zahoor 21-ARID-509

## Slide 2: Content
What is RAM and its types?
What is ROM and its types?
What is Cache hit and miss?

## Slide 3: Random Access Memory(RAM)
RAM is a type of computer memory used to store data and machine code that the computer is currently using.
RAM is a volatile memory, meaning that the data stored in RAM is lost when the power to the computer is turned off.
RAM stores the data temporarily while the computer is running, allowing the CPU to access it quickly and efficiently.
The speed of RAM affects how quickly the computer can access data, which can impact overall system performance.
The speed/frequency of RAM is measured in MHz(mega hertz).
Different types of RAM exist, including DRAM, SRAM, and SDRAM.

## Slide 4: DRAM
It is called "dynamic" because it needs to be constantly refreshed to maintain the stored data.
DRAM is organized into a grid of memory cells, each of which consists of a transistor and a capacitor. Each cell can store a single bit of data..
DRAM stores data in a capacitor that holds a charge, which represents a binary value of 1 or 0.
DRAM has a higher storage density than SRAM, another type of memory used in computers, but it is slower and requires more power to operate.
DRAM is used in personal computers and servers to mobile phones and embedded systems.
The average access time for DRAM is 60 nanoseconds

## Slide 5: Types of DRAM
SDRAM (Synchronous Dynamic Random Access Memory)
DDR SDRAM (Double Data Rate Synchronous Dynamic Random Access Memory)
DDR2 SDRAM (Double Data Rate 2 Synchronous Dynamic Random Access Memory)
DDR3 SDRAM (Double Data Rate 3 Synchronous Dynamic Random Access Memory)
DDR4 SDRAM (Double Data Rate 4 Synchronous Dynamic Random Access Memory)
DDR5 SDRAM (Double Data Rate 4 Synchronous Dynamic Random Access Memory)

## Slide 6: SDRAM
SDRAM which stands for Synchronous Dynamic Random Access Memory is a type of DRAM.
It synchronizes with the system bus clock, allowing for faster data transfer rates compared to asynchronous DRAM.
It uses a clock signal to synchronize the transfer of data between the memory controller and the memory chips.
It requires less power than earlier types of DRAM, making it more energy-efficient.
It is commonly used in desktop and laptop computers, servers, and other computing devices that require high-performance memory.

## Slide 7: DDR SDRAM
It can transfer data on both the rising and falling edges of the clock signal, effectively doubling the data transfer rate compared to SDR SDRAM.
DDR SDRAM operates at higher frequencies than SDR SDRAM, allowing for faster access times and higher bandwidths.
It has a higher peak data transfer rate compared to SDR SDRAM, which can improve the performance of memory-intensive applications such as gaming and multimedia.
DDR SDRAM has lower power consumption compared to earlier types of DRAM, making it more energy-efficient.
DDR SDRAM modules are available in different capacities and clock speeds, allowing for greater flexibility in configuring memory for specific applications.

## Slide 8: SDRAM Chart
Standard | Clock | Transfer Rate(GB/s) | Voltage(volts)
SDRAM | 66-133 MHz | 1.1 | 3.3
DDR SDRAM | 200 MHz | 3.2 | 2.5
DDR2 SDRAM | 400 MHz | 8.5 | 1.8
DDR3 SDRAM | 1.6 GHz | 17 | 1.5
DDR4 SDRAM | 3.2 GHz | 51.2 | 1.2

## Slide 9: SRAM
SRAM is a type of semiconductor memory that stores data using electronic circuits called flip-flops.
SRAM is called "static" because it doesn't require periodic refreshing to maintain data, unlike DRAM (Dynamic Random Access Memory).
SRAM can be accessed more quickly than DRAM, with access times typically measured in nanoseconds (ns).
SRAM is more immune to data corruption caused by environmental factors such as temperature and radiation than DRAM.
SRAM is commonly used in microprocessors, digital circuits that require high-speed, low-latency memory.
SRAM's access time can be around 10 nanoseconds.

## Slide 10: Read Only Memory(ROM)
ROM is non-volatile which means it retains its data even when the computer is turned off.
The data stored in ROM is not intended to be changed or modified, so it is considered "permanent" memory.
ROM is often used to store firmware, which is software that is embedded in hardware. For example, the BIOS (Basic Input/Output System) of a computer is typically stored in ROM.
ROM is typically slower than RAM (Random Access Memory), which is another type of computer memory.
Examples of ROM include the firmware in game cartridges for consoles like the Nintendo Gameboy, and the BIOS on a computer's motherboard.

## Slide 11: Types of ROM
Programmable ROM (PROM): This is a type of ROM that can be programmed by the user once using a special device called a ROM programmer. Once programmed, the data cannot be changed.
Erasable Programmable ROM (EPROM): This is a type of ROM that can be reprogrammed multiple times using ultraviolet light to erase the data. However, the process of erasing and reprogramming the memory is time-consuming and requires special equipment.
Electrically Erasable Programmable ROM (EEPROM): This is a type of ROM that can be erased and reprogrammed electronically, without the need for ultraviolet light. It is also sometimes called Flash memory.

## Slide 12: Comparison:
RAM
RAM stands for random access memory.
RAM data is volatile.
Data can be modified.
CPU can access data store on RAM.
RAM is faster.
RAM is more expensive.
ROM
Rom stands for read only memory.
ROM data is non-volatile.
Data cannot be modified.
Data to be copied from ROM to RAM, so that CPU can access its data.
ROM is slower.
ROM is cheaper than RAM.

## Slide 13: Cache Hit and Cache Miss
Cache: In computer architecture, a cache is a type of fast memory that is used to store frequently accessed data.
Cache hit: A cache hit occurs when the processor requests data and the data is found in the cache. This is advantageous because the cache is much faster than main memory, so the data can be accessed much more quickly.
Cache miss: A cache miss occurs when the processor requests data and the data is not found in the cache. This means that the processor has to retrieve the data from main memory, which is slower than accessing the data from the cache.
The goal of caching is to reduce the number of cache misses and increase the number of cache hits. This can significantly improve the performance of the system, particularly in applications that rely heavily on data access.

## Slide 14: BIOS
BIOS (Basic Input/Output System) is a firmware program that controls the basic input and output operations.
It’s key features are :
Booting the system: BIOS is responsible for booting up the computer and initializing the hardware components, such as the processor, memory, hard drive, and other peripherals.
CMOS setup: BIOS provides a CMOS setup utility, which allows the user to change system settings, such as the date and time, boot order, and hardware configurations.
Power management: BIOS manages the power settings of the computer and controls features such as sleep mode and hibernation.
BIOS boot order: BIOS determines the boot order of the devices, such as hard drives, optical drives, and USB drives, to boot the operating system.