## Slide 1
Computer Organization and Assembly Language CS

## Slide 2: COA
Up coming Labs (lab 02,03,04)
Labs in next class (follow mandatory requirements)
Lab resources:
  MASM 615
  Text pad editor
  Source codes
  Lab manual (hard copy)
Activities on group:
Quiz,Assig 01 solution posted
Result sheet ………. ????
Labs posted
Lecture 09 : Makeup class due to Moharrum leave

## Slide 3: Book reading : Supplementary !!!
Topics covered in this lecture are from these texts.
Computer organizations,9th edition,William stallings.
  Chapter 3 Computer Evolution & performance
  Read topic Performance assessments
  Chapter 4 A top level view of Computer function & interconnections
  Read topic Computer functions

## Slide 4
CPU Performance

## Slide 5: System Clock :

## Slide 6: Performance Assessment : Clock Speed
Key parameters:
  Performance, cost, size, security, reliability, power consumption
System clock speed
  In Hz or larger multiples of it.
  Clock rate, clock cycle, clock tick, cycle time.
Operations need to be synchronised.
Instruction execution in discrete steps.
  Fetch, decode, load and store, arithmetic or logical
  Usually require multiple clock cycles per instruction
Pipelining gives simultaneous execution of instructions
So, clock speed is not the whole story

## Slide 7: Instruction Execution Rate :
The effect of memory access, if taken into account
where p is no. of cycles needed to execute/decode instruction
m is number of memory reference needed
k is ratio b/w memory & processor cycle time.
The average CPI is defined as: clock per instruction

## Slide 8: Instruction Execution Rate :
Heavily dependent on
  Instruction set
  Compiler design
  Processor implementation
  Cache & memory hierarchy

## Slide 9: Instruction Execution Rate :
Millions of instructions per second (MIPS)
Millions of floating point instructions per second (MFLOPS)
What are the Benchmark programs & their importance in performance measurements?

## Slide 10: Instruction Performance
Clocks Per Instruction, CPI
  The average number of clock cycles each instruction takes to execute.
  Exercise:
  Which computer is faster?
Computer | Clock Cycle Time | CPI
A | 250 picoseconds | 2
B | 500 picoseconds | 1.2
  Solution : # of instructions in a program =
  CPU-A: CPU Execution Time = × × ps = ps
  CPU-B: CPU Execution Time = × × ps = ps
  Computer A is ( / ) = times faster than B

## Slide 11
  Exercise:
  Given 3 groups of instructions: A, B and C, it takes different clock cycles to execute an instruction within each group.
  Given the shown instruction mix, which code sequence is faster to execute?
 | Instruction Class |  | 
 | A | B | C
CPI | 1 | 2 | 3
Code | Instruction Count |  | 
 | A | B | C
Seq1 | 2 | 1 | 2
Seq2 | 4 | 1 | 1
  Seq1: CPU Execution Time = × + × + × = cycles
  Seq2: CPU Execution Time = × + × + × = cycles
  Seq1 average CPI = = cycles / instruction
  Seq2 average CPI = = cycles / instruction
  Seq2 is / = times faster than Seq1
Instruction Performance

## Slide 12: Class Example :
Consider a 400MHz processor executing instructions given in Table, taking specified CPI per instruction & instruction mix. Calculate effective CPI and MIPS for this processors?

## Slide 13: Your Turn !!!
Solution:

## Slide 14
AL instructions execution

## Slide 15: Ingredients of AL instruction :

## Slide 16: Ingredients of AL instruction :

## Slide 17: Ingredients of AL instruction :
stc (set carry flag, no operand)

## Slide 18: Ingredients of AL instruction :

## Slide 19: Instruction Encoding / Decoding
Instruction Format
Machine Language & Machine Code
  Machine code is what u store in memory.
  Encoding / decoding is done by CPU at
  the time of instruction execution.
Op code
Operands
ADD R1, R2, 47
5 1 2 2F
0101
0001
0010
00101111
5 1 2 2 F
Assembly Language
Machine Language

## Slide 20: Instruction Processing Components:

## Slide 21: Instruction Cycle : Basic steps
Basic two steps:
  Fetch
  Execute
  Detailed steps are discussed ahead.

## Slide 22: Fetch Cycle
Program Counter (PC) holds address of next instruction to fetch.
Processor fetches instruction from memory location pointed to by PC.
Increment PC.
  Unless told otherwise
Instruction loaded into Instruction Register (IR).
Processor interprets instruction and performs required actions.(Decoding of instruction.)

## Slide 23: Execute Cycle
Processor-memory
  data transfer between CPU and main memory
Processor- I/O
  Data transfer between CPU and I/O module
Data processing
  Some arithmetic or logical operation on data
Control
  Alteration of sequence of operations
  e.g. jump
Combination of above

## Slide 24: Instruction Execution : Detailed Example
Example :Designing, encoding/decoding an instruction execution

## Slide 25: Instruction Execution : Detailed Example

## Slide 26: Instruction Execution : Detailed Example

## Slide 27: Instruction Cycle : State Diagram

## Slide 28: Instruction cycle : Detailed steps
Detailed steps, involved in an instruction cycle, are as under

## Slide 29: THANKS ALL
          The End