## Slide 1: Week 03 : lecture 05
Computer Organization and Assembly Language
Quiz 01 on Rescheduled class Friday 24th Oct I.A

## Slide 2: Microprocessor Vs Microcontroller
What is a Microprocessor?
What is a Microcontroller?
A microprocessor is an electronic computers central processing unit (CPU) made from miniaturized transistors and other circuit elements on a single semiconductor integrated circuit (IC).
It performs arithmetic, logic and control operations. It contains a control unit, an arithmetic & logic unit, registers and links to store data and connect to peripherals.
Dedicated to performing one task. Integrates the memory and other features of a microprocessor.

## Slide 4: Microcomputer System
Microprocessor
(CPU)
Timing
Bus Control logic
Interface
Memory Module
Interface
Mass Storage Device
Interface
I/O Devices

## Slide 5: Microprocessor Architecture : Register file
Address
Data
Register File
ALU
Microprocessor
M E M O R Y

## Slide 6: Microprocessor Architecture : Register file

## Slide 7: Microprocessor Architecture : Register file

## Slide 8: Multi purpose Registers :
AL
 8 Bits 
AH
 8 Bits 
AX
BL
BH
BX
CL
CH
CX
DL
DH
DX
Accumulator Register
Base Register
Count Register
Division Register

## Slide 9: Multi purpose Registers :
Multipurpose registers:
8-bit register names used with register addressing: AH, AL, BH, BL, CH, CL, DH, and DL.
16-bit register names: AX, BX, CX, DX, SP, BP, SI, and DI.
80386 and above
32-bit register names are: EAX, EBX, ECX, EDX, ESP, EBP, EDI, and ESI.
64-bit mode register names are: RAX, RBX, RCX, RDX, RSP, RBP, RDI, RSI, and R8 through R15.
Note :Mixing of registers not allowed in assembler (Error)

## Slide 10
 16 Bits 
CS
Code Segment
DS
Data Segment
ES
Extra Segment
SS
Stack Segment
Multi purpose Registers :

## Slide 12: Instruction Format :
Instruction Format
  Mnemonic /abbreviation
  One or More Operands
Machine Code
  Binary form 1 , 0’s
Mnemonic /
Abbreviation Operands
Opcode Mode Operands