## Slide 2: Today’s lecture Breakdown:
I/O
Interrupts
Interrupt processing
Interrupt processing with priority

## Slide 3: Book reading : Supplementary !!!
Topics covered in this lecture are from these texts.
  Comp. Org. & Architecture,9th edition,Stallings
  For interrupts (Relevant to slides only)
  Read Chapter Top level view of Computer Functions,Section 2 (subpart) Interrupts
  For Input / Output (Relevant to slides only)
  Read Chapter Input / Output ,section 1,2
  Section 3,4 (Relevant details related to slides only)

## Slide 4
Input/output : I/O

## Slide 5: Input/output Problems
Why I/0’s not directly connected to system bus?
Wide variety of peripherals
  Delivering different amounts of data
  At different speeds
  In different formats
All slower than CPU and RAM
Need I/O modules

## Slide 6: Input/Output Module
Interface to CPU and Memory
Interface to one or more peripherals

## Slide 7: External Devices
An external device connected to an I/O module is called peripheral device or simply peripheral.
Human readable
  Screen, printer, keyboard
Machine readable
  Monitoring and control
  Disks,sensors,actuators etc.
Communication
  Modem
  Network Interface Card (NIC)
  Computers in a network.

## Slide 8: I/O Module Structure : Diagram

## Slide 9: I/O Module Function
I/O Module functioning could be explained by processor communication.
  Command decoding
  Data
  Status reporting
  Address Recognition
  Command decoding : I/O module accepts commands from processor on Control bus, Like read or write data.
  Data : Data is exchanged between processor and I/O module over data bus

## Slide 10: I/O Module Function
I/O Module functioning could be explained by processor communication.
  Command decoding
  Data
  Status reporting
  Address Recognition
  Status Reporting : I/O module are much slower than CPU and memory, they had to send STATUS signals to report their progress.
  For Example : BUSY or READY signal to report I/O status to processor

## Slide 11: I/O Module Function
I/O Module functioning could be explained by processor communication.
  Command decoding
  Data
  Status reporting
  Address Recognition
  Address Recognition : I/O module must receive multiple requests from processor thus I/O module must recognize and decode each address.
  For Example : After decoding I/O will identify, send control and data signal to selected peripheral.

## Slide 12: I/O Module Function
Control & Timing
CPU Communication
Device Communication
Data Buffering
Error Detection

## Slide 13: I/O Steps
CPU checks I/O module device status
I/O module returns status
If ready, CPU requests data transfer
I/O module gets data from device
I/O module transfers data to CPU
Variations for output
  Direct CPU Access
  Direct Memory Access

## Slide 14: CPU Viewpoint
Issue read command
Do other work
Check for interrupt at end of each instruction cycle
If interrupted:-
  Save context (registers)
  Process interrupt
    Fetch data & store

## Slide 15: Interfacing I/O & processors :

## Slide 16: Keyboard/Display Interfaces to 82C55A

## Slide 17
Interrupts

## Slide 18: Interrupts
Mechanism by which other modules (e.g. I/O) may interrupt normal sequence of processing
Program
  e.g. overflow, division by zero
Timer
  Generated by internal processor timer
  Used in pre-emptive multi-tasking (Preemptive scheduling enforces modularity in the sense that one thread cannot stop the progress of another thread, but if all threads share a single address space, then they can modify each other's memory accidentally)
I/O
  from I/O controller
Hardware failure
  e.g. memory parity error

## Slide 19: Transfer of Control via Interrupts

## Slide 20: Program Flow Control

## Slide 21: Simple Interrupt Processing

## Slide 22: Interrupt Cycle
Added to instruction cycle
Processor checks for interrupt
  Indicated by an interrupt signal
If no interrupt, fetch next instruction
If interrupt pending:
  Suspend execution of current program
  Save context
  Set PC to start address of interrupt handler routine
  Process interrupt
  Restore context and continue interrupted program

## Slide 23: Instruction Cycle with Interrupts

## Slide 24: Program Execution Timing : Short I/O Wait

## Slide 25: Instruction Cycle with Interrupts :

## Slide 26: Multiple Interrupts
Disable interrupts
  Processor will ignore further interrupts whilst processing one interrupt
  Interrupts remain pending and are checked after first interrupt has been processed
  Interrupts handled in sequence as they occur
Define priorities
  Low priority interrupts can be interrupted by higher priority interrupts
  When higher priority interrupt has been processed, processor returns to previous interrupt

## Slide 27: Multiple Interrupts – Sequential Processing

## Slide 28: Multiple Interrupts – Nested

## Slide 29: Priority Interrupt Execution : Example
Three I/O devices, a printer, a disk and data communication line with increasing priority of 2,4,and 5 respectively. Suppose all interrupt requires same execution time i.e 10ns. Following events occurs
Sr. # | Time (ns) | Activity/event
1 | t = 0 | User Program Starts
2 | t = 10 | Printer interrupt
3 | t = 15 | Communication interrupt
4 | t = 20 | Disk interrupt

## Slide 30: Time Sequence of Multiple Interrupts
t=0 | User Program Starts
t=10 | Printer interrupt
t =15 | Communication interrupt
t=20 | Disk interrupt

## Slide 31: Thanks ALL !!!